## Slide 1: Implementation of the EU-DEMO Exhaust Modelling Roadmap
S. Wiesen, L. Aho-Mantila, R. Osawa, F. Subba, M. Siccinio, F. Maviglia, M. Coleman, F. Koechl, H. Zohm, M. Bernert, S. Brezinsek, S. Dasbach, A. Kit, D. Matveev, J. Romazanov, M. Wischmeier and the EUROfusion DEMO central team (DCT)

## Slide 2: Power exhaust in a nutshell
ITPA Database, T. Eich et al NF 2013
From the lq-scaling: upstream q|| ~ 30 GW/m2 in DEMO (6 x higher than ITER)
 Unmitigated q^target: 300 MW/m2 for DEMO + radiation, neutrals, surface recombination
 Clearly exceeds the tolerable material limit q^max of 5-10 MW/m2 (actively cooled W-PFC).
DEMO: 30% radiation in core  XPR
Achievable radiation in SOL:
Faitsch 2020
… or other exhaust improved scenarios

## Slide 3: Baseline SOLPS-ITER fluid-kinetic model of EU DEMO divertor design
SOLPS-ITER D+He+Ar EU-DEMO reference, 21MA/4.9T scenario (2017), R=9m
76% of PSOL = 150MW dissipated by Ar radiation, fGW= 0.42
HFS fully detached LFS partial detachment
No XPR exposed
 2022: Scans of p0,div and cAr to assess operational window
W/m3
F. Subba et al NF 2020
qLFS
Prad
R.A. Pitts, et al, NME 2019
ITER
Role-model

## Slide 4
Revised impurity model, imp. CX processes, XPR regime
Fluid drifts SOL currents
Calibration fluid neutral model
Numerics: Grid convergence tests
Transport assessment A) lq~3mm (ITER like) B) lq > 3mm (e.g. QCE)
Geometry: SN Divertor Design, pumping, also: DDN topology & PWI
SOLPS-ITER, SN, D + He + Ar
Kinetic neutrals
Fluid neutrals
EU DEMO Roadmap 2022-2024

## Slide 5: Review and design of EU DEMO divertor shape
Inclusion of a liner, SOLPS-ITER being prepared
Assessment whether in terms of operational regime, the liner is advantageous w.r.t. He-exhaust and divertor performance (or otherwise too constraining in terms of the operational window for p0,div)
 2022: further review of divertor structure and impact on plasma, e.g. heat loads, neutral conductance, pumping, fuelling, erosion pattern of liner, etc
F. Subba et al, P147(C)
Divertor Optimization Shape & Engineering Systems

## Slide 6: EU DEMO Assessment of FW PWI employing ERO2.0
2021 equilibrium variant Axis location: R=9.47 m, Z=0.06 m
Plasma current: 18.3 MA
Btor on axis: 5.7 T
drsep
~ 6cm
Lifting the constraint of having the 2nd Xpoint not inside the vessel might provide flexibility to find an optimised (core) physics scenario, e.g high-d, QCE
Courtesy SOLPS-ITER grid, R. Osawa
A quantitative assessment of the impact on PWI and DEMO FW
Requires extension of SOLPS-ITER simulation grid up to first wall a) full extension, b) DDN topology (to include 2nd Xpoint)
Provide detailed plasma/neutral distributions to ERO2.0 Volumetric & Surface data, particle & heat fluxes, spectra, etc (EUROfusion TSVV7)

## Slide 7: Towards Reduced Models  Rapid Design, Systems Codes & Control
Towards improved figure-of-merits for e.g. heat-flux (i.e. detachment) and cZ  allows rapid design through systems code, e.g. radial builds, plant analysis, etc
Also: fast models needed for plasma control systems (PCS) in future devices
Current (reduced) models for exhaust based on incomplete scalings
 Extensions of 0D/1D models calibrated or “trained” by high-fidelity models for the edge/SOL
Siccinio, NF 2019
Based on
Martin scaling for PLH
Goldston & Reinke Scalings for cZ and lq
Conservative case:

## Slide 8: Towards fast Integrated modelling; HFPS-type
Integrated Model based on Engineering Parameters
Existing (reduced) SOL models are only valid for low-density or are not sufficiently reproducing details, e.g. Lengyel model  requires calibration or extensions c.f. A. Jaervinen, P027(G)
Existing pedestal models are quite “core-centric” e.g. include beta-dependence of pedestal width (e.g. EPED) Q: how to deal with line radiation in pedestal required in DEMO, frad,core ~ 30% or high nsep ?
Courstesy T. Luda et al, NF2020, EPS 2022

## Slide 9: Towards fast NN based surrogate models for interpolation of tokamak edge plasmas
S. Dasbach et al, P038(G)
NN trained by using data from SOLPS-ITER baseline simulations with fluid neutrals

## Slide 10: Developing deep learning algorithms for determining ne,sep
A. Kit et al, P226(F)
NN Trained by using Data from JET
Pedestal database Frassinetti NF2021
Representation learning: Learn a latent variable with prior that represents profiles
with variational autoencoder (VAE) framework.
Futhermore, also a condition prior
on machine parameters, , i.e., learn
 domain invariant VAE (DIVA)

## Slide 11: Summary
The conceptional design phase for EU-DEMO implies a revision of the exhaust modelling roadmap until 2024.
For the purpose of identifying a controllable exhaust scenario to be employed in EU-DEMO, the required physics foundation of candidate regimes must be re-assessed by using validated numerical tools  SOLPS-ITER EU-DEMO database a la ITER  Towards revised physics model: fluid drifts and neutral kinetics, allowing for charge exchange for impurities enhancing non-coronal radiation levels in the edge.
A multi-fidelity approach advantageous to complement the final model to be composed for exploring the EU-DEMO exhaust operational window.
An integrated & optimised core-edge scenario is needed compatible to maintain energy dissipation fraction of up to 95% in the edge, of which 30% in core  extension of HFPS by integrating fast & calibrated exhaust models
Recent activities on development of fast NN-based surrogate exhaust models  promising and might become relevant for HFPS, fast PCS & systems codes

## Slide 12: backup

## Slide 13: Dissipation by radiation – tailoring of radiation field – the XPR
Various seeding impurities possible N (div), Ne (SOL), Ar (SOL+ped), Kr (core), Xe
Xpoint Radiator (XPR), offers: - full detachment - large dissipation fraction (up to 100%) - Controllability demonstrated (AUG, TCV) - ELM suppressed regime accessible - compatible with good confinement
Gloeggler 2020
S. Wiesen | IEK-4 Theory Seminar | Feb 17th , 2022| Page 13
T. Pütterich, NF2019
ASDEX-Upgrade stable controlled N-seeding XPR
M. Bernert T. Bosman et al P037(G)

## Slide 14: Role Model: ITER Divertor Design studies: metal wall & SOLPS-ITER
R.A. Pitts, E. Kaveeva, V. Rozhanski, S. Wiesen, X. Bonnin et al, NME 2019
PSOL=100MW
control parameter 1
control parameter 2

## Slide 15: Re-attachment in DEMO
The maximum tolerable steady-state HF on the current DEMO SN divertor plate is 10-20 MW/m2. [J.H. You, G1 review mtg] This value can be achieved only in detached plasma conditions (with seeded impurities).
In case of accidental divertor reattachment, the divertor reaches burn-out (leading to an in-vessel LOCA) in about 3 sec.
Siccinio, NF 2019
RACLETTE: 10s HF ramp 10..70 MW/m2
S. Wiesen | IEK-4 Theory Seminar | Feb 17th , 2022| Page 15

## Slide 16: Re-attachment in DEMO
What about “fast termination”?
A fast plasma shutdown (like in ITER) at full current would pose unacceptable risks on the machine integrity [Maviglia, NME 2021],[Lehnen, IAEA 2016].
In parallel, the current cannot be ramped down faster than ~0.2 MA/s without losing vertical stability control. (the increase of ramp down rate with the use of IVC is presently being investigated)
[Siccinio, FED 2020]
ITER
DEMO
[Lehnen, IAEA 2016]
S. Wiesen | IEK-4 Theory Seminar | Feb 17th , 2022| Page 16

## Slide 17: Towards fast NN based surrogate models for interpolation of tokamak edge plasmas
S. Dasbach et al, P038(G)
NN trained by using data from SOLPS-ITER baseline simulations with fluid neutrals
Also alternative approaches possible:
Surrogate kinetic models, i.e. replacing the direct coupling to EIRENE (slow convergence) in SOLPS-ITER with trained NN for particle sources  faster convergence
Online learning: start from trained fluid-only NN surrogate for SOLPS-ITER and allow incrementally for more physics
Also: time-dependent models, e.g. SOLPS-ITER calibrated fast NN based 1D divertor model predictors for transients  plasma control (Y. Poels, J. Koenders, G. Derks, M. van Berkel et al)

## Slide 18: Replace the kinetic neutral model with a fast NN surrogate
Input
Kinetic Neutrals
Fluid Plasma
Kinetic Neutrals
Fluid Plasma
Kinetic Neutrals
…
Input
Surrogate
Fluid Plasma
Surrogate
Fluid Plasma
Surrogate
…
S. Dasbach et al, P038(G)

## Slide 19: Replace the kinetic neutral model with a fast NN surrogate
The precision would be sufficient if below Monte Carlo noise of reference model
S. Dasbach et al, P038(G)